Standard Auto Lift & Equipment Inc

Please call 1-888-839-8899

STDGA-9000 series Four Post Lift is produced in USA.

We are offering FREE with the purchase of this lift the Jack Tray and 3 Drip Trays*.

Feature:

• Made with North American Steel

• Powder coat finish

• SPX Power unit

• Max 9,000lbs Lifting Capacity

• 5" × 5" posts

• 6" × 6" sliding collars

• 36" aluminum approach ramps

• 3/8” Galvanized steel cable

• 3/16” Diamond Steel Runway

• Single Point Manual Lock Release

• 5 year warranty on the structure and 1 year on the hydraulics parts.

Specifications:

| Model | STDGA-9000ST | STDGA-9000XLT |
| --- | --- | --- |
| Max Lifting Capacity | 9,000lbs | 9,000lbs |
| Overall Height of Corner Posts | 93" | 105" |
| Max Height to Top of Track on Lock | 75-1/2" | 86-1/2" |
| Max Clearance Under Deck on Lock | 71" | 82" |
| Size of Column | 5" × 5" x 1/4”Tube | 5" × 5" x 1/4” |
| Cross Arm | 2” x 4” x 1/4” | 2” x 4” x 1/4” |
| Base Plate | 12” x 12” x 5/8” | 12" × 12" x 5/8” |
| Track Length | 170" | 192" |
| Track Thickness(US Style) | 4-1/2” (3/16” Dia. Steel) | 4-1/2” (3/16" Diamond Steel) |
| Track Width | 19-1/2" | 19-1/2" |
| Floor Space Footprint | L 182" × W 113" | L 203" × W 119" |
| Overall Width Outside Post | 108" | 114" |
| Overall Length / with 36" App. Ramps | 182" / 213" | 203" / 236" |
| Outside Width Track to Track | 76-1/2" | 76-1/2" |
| Width Between Tracks / Rails | 37-1/2" / 34-3/4" | 37-1/2" / 34-3/4" |
| Between the Post Width | 98" | 104" |
| Power Electric/Hydraulic | 120 Volt 30 Amp | 120 Volt 30 Amp |
| Shipping Weight | 1880 lbs. | 2250 lbs. |

*3 Drip trays are made in China

*220V available on request

*Specifications Subject to Change Without Notice